## Slide 1: Secure Group Key Distribution in Constrained Environments with IKEv2
2017 IEEE Conference on Dependable and Secure Computing
Taipei • Taiwan
Nils gentschen Felde, Tobias Guggemos, Tobias Heider and Dieter Kranzlmüller
MNM-Team
Ludwig-Maximilians-Universität München

## Slide 2: Typical IoT Management Architecture
ID Management
Access Management
Key Management
?????

## Slide 3: Question
In this work, we focus on the problem of Key Management in the special case of group communication
includes most major IoT-related communication models
Securing groups can help securing IoT in general
Group key distribution also enables universal key distribution

## Slide 4: Challenge of interoperability
Re-using existing solution and make them suitable for constrained environments

## Slide 5: Re-use existing solutions
Requires specifications
for Group Managment
Widely used and standardized for constrained networks

## Slide 6: Re-use existing solutions
Especially designed for group managment
7 messages for key distribution  Too heavy for constrained environments

## Slide 7: Re-use existing solutions
No central authority
- Does not scale for large groups - Not useful for WANs

## Slide 8: Re-use existing solutions
Reduces Network and computing overhead
Problem with trust in dynamic environments

## Slide 9: Re-use existing solutions
- Designed for GKM - Based on IKEv2, which is optimized for IoT
Not widely supported

## Slide 10: Evaluation
How does G-IKEv2 perform on constrained environments

## Slide 11: Testbed
Devices | Arduino Uno | Arduino M0+ | Arduino Due
Architecture | ATmega328 | ARM Cortex-M0+ | ARM Cortex-M3
CPU | 16 MHz | 48 MHz | 84 MHz
RAM | 2 KB | 32 KB | 96 KB
Flash | 32 KB | 256 KB | 512 KB
Operating System | RIOT OS | RIOT OS | RIOT OS

## Slide 12: The G-IKEv2 Protocol

## Slide 13: Implementation

## Slide 14: Evaluation
Asymmetric EC Diffie Hellman
Only ones for initial connection with key server

## Slide 15: Conclusion
Group Management will become more important for IoT
GKM is widely studied, but underrepresented for constrained scenarios
IKEv2 is already used for Key Distribution in Wireless Networks (e.g. 802.15.4)
 G-IKEv2 is an interesting option for group key management in IoT scenarios

## Slide 16: The End
MNM-Team
Ludwig-Maximilians-Universität München
http://www.mnm-team.org/projects/embedded
Curious?