## Slide 1: Internet Routing (cont.)

## Slide 2: Outline
Routing hierarchy
Internet structure
External BGP (E-BGP)
Internal BGP (I-BGP)
BGP details

## Slide 3: Routing Hierarchies
Flat routing doesn’t scale
  Each node cannot be expected to have routes to every destination (or destination network)
Key observation
  Need less information with increasing distance to destination
Two different approaches for routing
  The area hierarchy
  The landmark hierarchy (an alternative)

## Slide 4: Areas
Divide network into areas
  Areas can have nested sub-areas
  Constraint: no path between two sub-areas of an area can exit that area
Hierarchically address nodes in a network
  Sequentially number top-level areas
  Sub-areas of area are labeled relative to that area
  Nodes are numbered relative to the smallest containing area

## Slide 5: Outline
Routing hierarchy
Internet structure
External BGP (E-BGP)
Internal BGP (I-BGP)
BGP details

## Slide 6: Internet’s Area Hierarchy
Autonomous System (AS)?
  A set of routers under a single technical administration, using an interior gateway protocol (IGP) and common metrics to route packets within the AS and using an exterior gateway protocol (EGP) to route packets to other AS’s
Each AS assigned unique ID
AS’s peer at network exchanges

## Slide 7: Routing
Within area
  Each node has routes to every other node
Outside area
  Each node has routes for other top-level areas only
  Route Inter-area packets to nearest appropriate border router
Can result in sub-optimal paths

## Slide 8: History: IGP
Most common IGPs:
  RIP: Routing Information Protocol (v1: 1988, v2: 1994)
  OSPF: Open Shortest Path First (1988 - 1998)
  IS-IS: Intermediate system to intermediate system (mid to end 90s)
  EIGRP: Enhanced Interior Gateway Routing Protocol (Cisco proprietary, mid-80s)

## Slide 9: History: EGP
Mid-80s: EGP
  Reachability protocol (no shortest path)
  Did not accommodate cycles (tree topology)
  Evolved when all networks connected to NSF backbone
Result: BGP introduced as routing protocol
  Latest version = BGP 4
  BGP-4 supports CIDR
  Primary objective: connectivity not performance

## Slide 10: A Logical View of the Internet?
After looking at RIP/OSPF descriptions
  End-hosts connected to routers
  Routers exchange messages to determine connectivity
NOT TRUE!
R
R
R
R
R

## Slide 11: A Logical View of the Internet?
R
R
R
R
R
RIP/OSPF not very scalable  area hierarchies
But, ISP’s aren’t equal
  Size
  Connectivity
NOT TRUE EITHER!
ISP
ISP

## Slide 12: A Logical View of the Internet
Tier 1 ISP
  “Default-free” with global reachability info
Tier 2 ISP
  Regional or country-wide
Tier 3 ISP
  Local
Tier 1
Tier 1
Tier 2
Tier 2
Tier 2
Tier 3
Customer
Provider

## Slide 13: Transit vs. Peering
ISP X
ISP Y
ISP Z
ISP P
Transit ($)
Transit ($$$)
Transit ($$ 1/2)
Transit ($$)
Peering
Transit ($$$)
Transit ($)
Transit ($$)
Transit ($$$)

## Slide 14: Outline
Routing hierarchy
Internet structure
External BGP (E-BGP)
Internal BGP (I-BGP)
BGP details

## Slide 15: Choices
Link state or distance vector?
  No universal metric – policy decisions
Problems with distance-vector:
  Bellman-Ford algorithm may not converge
Problems with link state:
  Metric used by routers not the same – loops
  LS database too large – entire Internet
  May expose policies to other AS’s

## Slide 16: Solution: Distance Vector with Path
Each routing update carries the entire path
Loops are detected as follows:
  When AS gets route check if AS already in path
    If yes, reject route
    If no, add self and (possibly) advertise route further
Advantage:
  Metrics are local - AS chooses path, protocol ensures no loops

## Slide 17: Interconnecting BGP Peers
BGP uses TCP to connect peers
Advantages:
  Simplifies BGP
  No need for periodic refresh - routes are valid until withdrawn, or the connection is lost
  Incremental updates
Disadvantages
  Congestion control on a routing protocol?
  Poor interaction during high load

## Slide 18: Hop-by-hop Model
BGP advertises to neighbors only those routes that it uses
  Consistent with the hop-by-hop Internet paradigm
  e.g., AS1 cannot tell AS2 to route to other AS’s in a manner different than what AS2 has chosen

## Slide 19: Policy with BGP
BGP provides capability for enforcing various policies
Policies are not part of BGP: they are provided to BGP as configuration information
BGP enforces policies by choosing paths from multiple alternatives and controlling advertisement to other AS’s

## Slide 20: Examples of BGP Policies
A multi-homed AS refuses to act as transit
  Limit path advertisement
A multi-homed AS can become transit for some AS’s
  Only advertise paths to some AS’s
An AS can favor or disfavor certain AS’s for traffic transit from itself

## Slide 21: BGP Common Header
Length (2 bytes)
Type (1 byte)
0
1
2
3
Marker (security and message delineation)
16 bytes
Types: OPEN, UPDATE, NOTIFICATION, KEEPALIVE

## Slide 22: BGP Messages
Open
  Announces AS ID
  Determines hold timer
    interval between keep_alive or update messages
    zero interval implies no keep_alive
Keep_alive
  Sent periodically to ensure connectivity.
  Sent in place of an UPDATE message
Notification
  Used for error notification
  Closes TCP connection immediately after notification

## Slide 23: BGP UPDATE Message
List of withdrawn routes
Network layer reachability information
  List of reachable prefixes
Path attributes
  Origin
  Path
  Metrics
All prefixes advertised in message have same path attributes

## Slide 24: Path Selection Criteria
Information based on path attributes
Attributes + external (policy) information
Examples:
  Hop count
  Policy considerations
    Preference for AS
    Presence or absence of certain AS
  Path origin
  Link dynamics

## Slide 25: LOCAL PREF
Local (within an AS) mechanism to provide relative priority among BGP routers
R1
R2
R3
R4
I-BGP
AS 256
AS 300
Local Pref = 500
Local Pref =800
AS 100
R5
AS 200

## Slide 26: LOCAL PREF – Common Uses
Handle traffic directed to multi-homed transit customers
  Allows provider to prefer a route
Peering vs. transit
  Prefer to use peering connection, why?
In general, customer > peer > provider
  Use LOCAL PREF to ensure this

## Slide 27: AS_PATH
List of traversed AS’s
AS 500
AS 300
AS 200
AS 100
180.10.0.0/16 300 200 100
170.10.0.0/16 300 200
170.10.0.0/16
180.10.0.0/16

## Slide 28: CIDR and BGP
AS X
197.8.2.0/24
AS Y
197.8.3.0/24
AS T (provider)
197.8.0.0/23
AS Z
What should T announce to Z?

## Slide 29: Options
Advertise all paths:
  Path 1: through T can reach 197.8.0.0/23
  Path 2: through T can reach 197.8.2.0/24
  Path 3: through T can reach 197.8.3.0/24
But this does not reduce routing tables! We would like to advertise:
  Path 1: through T can reach 197.8.0.0/22
Notes: What are some choices?

## Slide 30: Sets and Sequences
Problem: what do we list in the route?
  List T: omitting information not acceptable may lead to loops
  List T, X, Y: misleading, appears as 3-hop path
Solution: restructure AS Path attribute as:
  Path: (Sequence (T), Set (X, Y))
  If Z wants to advertise path:
    Path: (Sequence (Z, T), Set (X, Y))
  In practice used only if paths in set have same attributes

## Slide 31: Multi-Exit Discriminator (MED)
Hint to external neighbors about which path into an AS to prefer
  Non-transitive attribute (we will see later why)
  Different AS choose different scales
Used when two AS’s connect to each other in more than one place

## Slide 32: MED
Hint to R1 to use R3 over R4 link
Cannot compare AS40’s values to AS30’s
R1
R2
R3
R4
AS 30
AS 40
180.10.0.0
MED = 120
180.10.0.0
MED = 200
AS 10
180.10.0.0
MED = 50
Notes: Where would you use this? Between ISPs? At edges?

## Slide 33: MED
SF
NY
ISP1 ignores MED from ISP2
ISP2 obeys MED from ISP1
ISP2 ends up carrying traffic most of the way
ISP1
ISP2
e.g. used in peering or provider/subscriber scenarios
can lead to unfairness: may force an ISP to carry more traffic than its partner:

## Slide 34: Other Attributes
ORIGIN
  Source of route (IGP, EGP, other)
NEXT_HOP
  Address of next hop router to use

## Slide 35: Decision Process
Processing order of attributes:
  Select route with highest LOCAL-PREF
  Select route with shortest AS-PATH
  Apply MED (if routes learned from same neighbor)
  ....

## Slide 36: Outline
Routing hierarchy
Internet structure
External BGP (E-BGP)
Internal BGP (I-BGP)
BGP details

## Slide 37: Internal vs. External BGP
R3
R4
R1
R2
E-BGP
AS1
AS2
BGP can be used by R3 and R4 to learn routes
How do R1 and R2 learn routes?
  Option 1: Inject routes in IGP
    Only works for small routing tables
  Option 2: Use I-BGP

## Slide 38: Internal BGP (I-BGP)
Same messages as E-BGP
Different rules about re-advertising:
  Prefix learned from E-BGP can be advertised to I-BGP neighbor and vice-versa, but
  Prefix learned from one I-BGP neighbor cannot be advertised to another I-BGP neighbor
  Reason: no AS PATH within the same AS and thus danger of looping.

## Slide 39: Internal BGP (I-BGP)
R3
R4
R1
R2
E-BGP
I-BGP
AS1
AS2
R3 can tell R1 and R2 prefixes from R4
R3 can tell R4 prefixes from R1 and R2
R3 cannot tell R2 prefixes from R1
R2 can only learn via a direct connection to R1
Result: I-BGP routers must be fully connected (via TCP)!
  Contrast: E-BGP sessions usually map to physical links

## Slide 40: Link Failures
Two types of link failures:
  Failure on an E-BGP link
  Failure on an I-BGP Link
These failures are treated completely different in BGP
Why?

## Slide 41: Failure of an E-BGP Link
AS1
R1
AS2
R2
Physical link
E-BGP session
138.39.1.1/30
138.39.1.2/30
If the link R1-R2 goes down
  The TCP connection breaks
  BGP routes are removed
This is the desired behavior

## Slide 42: Failure on an I-BGP Link
R1
R2
R3
Physical link
I-BGP connection
138.39.1.1/30
138.39.1.2/30
Link R1-R2 down => R1 and R2 can still exchange traffic
The indirect path through R3 must be used
E-BGP and I-BGP use different conventions with respect to TCP endpoints
  E-BGP: no multihop -- I-BGP: multihop OK

## Slide 43: Outline
Routing hierarchy
Internet structure
External BGP (E-BGP)
Internal BGP (I-BGP)
BGP Details
  Multi-Homing
  Stability Issues

## Slide 44: Multi-homing
Multi-homing:
  Network has several connections to the Internet.
Improves reliability and performance:
  Can accommodate link failure
  Bandwidth is sum of links to Internet
Challenges
  Getting policy right (MED, etc..)
  Addressing

## Slide 45: Multi-homing to Multiple Providers
Major issues:
  Addressing
  Aggregation
Customer address space:
  Delegated by ISP1
  Delegated by ISP2
  Delegated by ISP1 and ISP2
  Obtained independently
ISP1
ISP2
ISP3
Customer

## Slide 46: Address Space from one ISP
Customer uses address space from ISP1
ISP1 advertises /16 aggregate
Customer advertises /24 route to ISP2
ISP2 relays route to ISP1 and ISP3
ISP2-3 use /24 route
ISP1 routes directly
Problems with traffic load?
138.39/16
138.39.1/24
ISP1
ISP2
ISP3
Customer

## Slide 47: Pitfalls
ISP1 aggregates to a /19 at border router to reduce internal tables.
ISP1 still announces /16.
ISP1 hears /24 from ISP2.
ISP1 routes packets for customer to ISP2!
Workaround: ISP1 must inject /24 in I-BGP.
138.39.0/19
138.39/16
ISP1
ISP2
ISP3
Customer
138.39.1/24

## Slide 48: Address Space from Both ISPs
ISP1 and ISP2 continue to announce aggregates
Load sharing depends on traffic to two prefixes
Lack of reliability: if ISP1 link goes down, part of customer becomes inaccessible.
Customer may announce prefixes to both ISPs, but still problems with longest match as in case 1.
138.39.1/24
204.70.1/24
ISP1
ISP2
ISP3
Customer

## Slide 49: Independent Address Space
Offers the most control, but at the cost of aggregation.
Still need to control paths
Many ISP’s ignore advertisements of less than /19
ISP1
ISP2
ISP3
Customer

## Slide 50: Outline
Routing hierarchy
Internet structure
External BGP (E-BGP)
Internal BGP (I-BGP)
BGP Details
  Multi-Homing
  Stability Issues

## Slide 51: Signs of Routing Instability
Monitored BGP messages at major exchanges
Orders of magnitude more updates than expected
  Bulk: duplicate withdrawals
    Stateless implementation of BGP – did not keep track of information passed to peers
    Impact of few implementations
  Strong frequency (30/60 sec) components
    Interaction with other local routing/links etc.

## Slide 52: Route Flap Storm
Overloaded routers fail to send Keep_Alive message and marked as down
I-BGP peers find alternate paths
Overloaded router re-establishes peering session
Must send large updates
Increased load causes more routers to fail!

## Slide 53: Route Flap Dampening
Routers now give higher priority to BGP/Keep_Alive to avoid problem
Associate a penalty with each route
  Increase when route flaps
  Exponentially decay penalty with time
When penalty reaches threshold, suppress route

## Slide 54: BGP Limitations: Path exploration
AS 0
AS 2
AS 1
R
(*R,1R,2R)
(0R,*R,2R)
(0R,1R,*R)

## Slide 55: BGP Limitations: Path exploration
AS 0
AS 2
AS 1
R
(-,*1R,2R)
(*0R,-,2R)
(*0R,1R,-)
W
W
W



(*R,1R,2R)
(0R,*R,2R)
(0R,1R,*R)

## Slide 56: BGP Limitations: Path exploration
AS 0
AS 2
AS 1
R
(-,*1R,2R)
(-,-,*2R)
(01R,*1R,-)
01R
01R



(-,*1R,2R)
(*0R,-,2R)
(*0R,1R,-)

## Slide 57: BGP Limitations: Path exploration
AS 0
AS 2
AS 1
R
(-,-,*2R)
(-,-,*2R)
(*01R,10R,-)
10R
10R



(-,*1R,2R)
(-,-,*2R)
(01R,*1R,-)

## Slide 58: BGP Limitations: Path exploration
AS 0
AS 2
AS 1
R
(-,-,-)
(-,-,*20R)
(*01R,12R,-)
20R
20R



(-,-,*2R)
(-,-,*2R)
(*01R,10R,-)

## Slide 59: BGP Limitations: Path exploration
AS 0
AS 2
AS 1
R
(-,*12R,-)
(-,-,*20R)
(*01R,-,-)
12R
12R



(-,-,-)
(-,-,*20R)
(*01R,10R,-)

## Slide 60: BGP Limitations: Path exploration
AS 0
AS 2
AS 1
R
(-,*12R,21R)
(-,-,-)
(*01R,-,-)
21R
21R
(-,*12R,-)
(-,-,*20R)
(*01R,-,-)




## Slide 61: BGP path exploration
Can possible explore every possible path through network  (n-1)! Combinations
Limit between update messages (MinRouteAdver) reduces exploration
  Forces router to process all outstanding messages
Typical Internet failover times
  New/shorter link  60 seconds
    Results in simple replacement at nodes
  Down link  180 seconds
    Results in search of possible options
  Longer link  120 seconds
    Results in replacement or search based on length