## Slide 1: An Overview of Internet Routing Protocols
Notes: Please email me with comments on this course.
The web site contains these slides, course information, and interesting routing related links.
This is intended to be a one day course.

## Slide 2: Outline
IP Forwarding vs. Routing
What is an IP routing protocol?
A peek at three of them :
  RIP
  OSPF
  BGP
Care and feeding of routing protocols
is an important part of network
management in ISPs

## Slide 3: IP Forwarding Process
Forwarding Process
IP Forwarding Table
Router
1. Remove a packet
from an input
queue
3. Match packet’s
destination to
a table entry
2. Check for sanity,
decrement TTL
field
4. Place packet on
correct output
queue
Notes: See RFC 1264 “Internet Engineering Task Force Internet Routing Protocol Standardization Criteria.” 1991

## Slide 4: IP Forwarding Table
Destination
Next Hop
Interface
Net A
Net B
Net C, Host 3
Router 1
Direct
Router 2
Router 1
Default
INT 7
INT 7
INT 3
INT 4
A destination is
either a network,
a host, or a “gateway
of last resort”
The next hop is
either a directly
connected network or a
router on a directly
connected network
A physical interface
Notes: Often called routing table

## Slide 5: Routing = Implementing End-to-End Paths with Next Hop Forwarding Tables
R
R
R
A
B
C
D
R1
R2
R3
R4
R5
E
Dest.
Nxt Hop
R4
R3
R3
R4
Direct
R4
Dest.
Nxt Hop
A
B
C
D
E
default
R2
R2
Direct
R5
R5
R2
Dest.
Nxt Hop
A
B
C
D
E
default
R1
Direct
R3
R1
R3
R1
Default to
upstream
router
A
B
C
D
E
default
Notes: Assume tables populated by magic.
If we assume all forwarding tables are populated in a consistent way, then there is no real danger in confusing “end to end route” with a “next hop route.” Of course, the study of routing techniques explores ways to ensure that this is a safe assumption.

## Slide 6: How are Forwarding Tables Populated?
Statically
Dynamically
Routers exchange information using ROUTING PROTOCOLS that compute “best” routes
Administrator
manually configures
table entries
In practice : a mix of these….
+ More control
+ Not restricted to
destination-based
forwarding
- Doesn’t scale
- Slow to adapt to
network failures
+ Can rapidly adapt to changes
in network topology
+ Can be made to scale well
- Complex distributed algorithms
- Consume CPU, Bandwidth, Memory
- Debugging can be hell
- Current protocols are destination-based
Notes: The “routing problem” arises in ALL networking technologies. Solutions
vary depending on the specific technologies and how they are employed.
I would like to do study of the techniques used in telegraphy networking. Since “datagrams” get their name from “telegrams” it would be fun to compare the different routing techniques used. Anyone want to join me on this?
Note that some texts on Data Networking (especially those that are ATM centric?) use the term “Static routing” to mean what we are calling Dynamic
routing. “Adaptive routing” is used to describe protocols that route around network congestion.

## Slide 7: Bad Things Can Happen
R1
R2
Dest.
Nxt Hop
A
:
R2
:
Dest.
Nxt Hop
A
:
R1
:
Loops are routing
problems, not
forwarding problems

## Slide 8: The Most Common Routing Protocols
Routing protocols exchange network
reachability information between routers.
IP (and ICMP)
TCP
UDP
BGP
RIP
OSPF
EIGRP
IS-IS
Cisco proprietary
Notes: This slide illustrates the Routing Protocol Encapsulation
BGP : TCP port number 179.
RIP : UDP port number 520.
OSPF : IP protocol number 89.
One reason why routing protocols are not more well-known is that they run on routers and do not provide services directly to end-user applications. These protocols are however VERY familiar to network administrators. They keep the network connected! LANS generally deal with OSPF or RIP. ISPs and backbone network providers deal with BGP. In fact, they devote considerable resources to the care and feeding of BGP.

## Slide 9: What is a Routing Process?
Routing
Process
Protocol-Specific
Routing Table
import
information
from other
routers
export
information
to other
routers
IP Forwarding Table
Router
Manual configuration
Notes: See RFC 1264 “Internet Engineering Task Force Internet Routing Protocol Standardization Criteria.” 1991
“Other routers” is usually a routers immediate neighbors. Why? To talk
to more distant routers requires routing! We will see that BGP uses TCP
connections within an autonomous system, but it can do this because it
assumes that the autonomous system has a local routing system.

## Slide 10: Many routing processes can run on a single router
IP Forwarding Table
RIP Process
BGP Process
OSPF Process
OSPF
Domain
RIP
Domain
BGP
Interaction is manually configured

## Slide 11: Architecture : Interior vs. Exterior Routing Protocols
IGP
IGP
IGP
EGP
EGP
EGP
AS 100
AS 200
AS 300
Interior Gateway Protocol (IGP) :
for connectivity inside an
autonomous system.
Exterior Gateway Protocol (EGP) :
for connectivity between
autonomous systems
OSPF, RIP,
EIGRP, IS-IS
BGP
Friendly world,
full connectivity,
rapid convergence
Hostile world,
restricted connectivity,
stability,
scalability
Notes: IGPs : should calculate “best routes” and quickly adapt to topology changes.
EGP: enforce routing policies, including aggregation.

## Slide 12: Basic Model: Finding Shortest Paths
A
D
E
C
B
100
100
20
20
80
80
20
20
10
10
10
10
10
10
Source
50
30
20
30
Find paths from a source
to all other nodes that
minimizes sum of arc
metrics
Arc metrics are
statically provisioned
IP routing protocols
DO NOT route around
network congestion!

## Slide 13
Arcs,
Nodes,
Arc Weights
Directed Graph
data structures
+
Algorithm
Dijkstra’s or
Bellman-Ford
=
Solution to shortest
path problem
How can shortest path computation
be decentralized and performed
by many cooperating routers?
Distribute path
computation.
Keep only local
link data.
Distribute all
link data.
Perform path
computations
locally.
RIP, EIGRP,
BGP
OSPF, IS-IS,
IDPR
Technology : Distance Vector vs. Link State Protocols
Distance Vector
Link State
Notes: While RIP is bases on a distributed processing algorithm (routers send results of intermediate computations to neighbors, keeping link data local) OSPF is bases on local processing and data distribution (Links states are made public
and redistributed --- best path computations are done locally ate each router).
Can use ANY algorithm --- bust most common is Dijkstra’s Shortest Path
First (a “greedy” algorithm used to solve the “single source shortest path” problem in directed graphs with non-negative edge weights.)

## Slide 14: RIP
RIP = Routing Information Protocol
Does not scale well, designed for small LANs
Is a “distance vector protocol”
Very simple, easy to configure, easy to implement
Limitations in terms of scaling, convergence, etc… not used anymore!

## Slide 15: RIP Routing Table
Destination
Next Hop
Metric
Net A
Net B
Net C, Host 3
Router 1
Direct
Router 2
Router 1
Default
3
5
0
A destination is
either a network,
a host, or a “gateway
of last resort”
The next hop is
either a directly
connected network or a
directly connected router
Measures how many
“hops away” is the
destination
0
Notes: Often called routing table

## Slide 16: Basic RIP Protocol
Periodically exchange list
of destinations and metrics
with all neighboring routers
Dest.
Metric
A
B
C
3
0
5
Dest.
Metric
A
E
F
1
2
0
RIP routers exchange
their entire “distance
vector” every 30
seconds

## Slide 17: Distance Vector Routing Algorithm
iterative:
continues until no nodes exchange info.
self-terminating: no “signal” to stop
asynchronous:
nodes need not exchange info/iterate in lock step!
distributed:
each node communicates only with directly-attached neighbors
Distance Table data structure
each node has its own
row for each possible destination
column for each directly-attached neighbor to node
example: in node X, for dest. Y via neighbor Z:
D (Y,Z)
X
distance from X to
Y, via Z as next hop
c(X,Z) + min {D (Y,w)}
Z
w
=
=
Notes: <number>
<footer>
<header>
<date/time>

## Slide 18: Distance Table: example
A
E
D
C
B
7
8
1
2
1
2
D ()
A
B
C
D
A
1
7
6
4
B
14
8
9
11
D
5
5
4
2
E
cost to destination via
destination
D (C,D)
E
c(E,D) + min {D (C,w)}
D
w
=
=
2+2 = 4
D (A,D)
E
c(E,D) + min {D (A,w)}
D
w
=
=
2+3 = 5
D (A,B)
E
c(E,B) + min {D (A,w)}
B
w
=
=
8+6 = 14
(loop)
(loop)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 19: Basic RIP Protocol (cont.)
c
Neighbor N
Is Dest. A in my RIP Table?
Receive
Dest.
Metric
A
m
From Neighbor N
Dest.
Metric
A
m + c
Nxt Hop
N
Add
to RIP table
Is m + c less than current
metric for Dest. A?
NO
Yes
Yes
Dest.
Metric
A
m + c
Nxt Hop
N
Replace current entry with
in RIP table
Is N my next hop for Dest. A and
m + c is not the current metric?
NO
Yes
Trust your neighbor...

## Slide 20: Distance table gives routing table
D ()
A
B
C
D
A
1
7
6
4
B
14
8
9
11
D
5
5
4
2
E
cost to destination via
destination
A
B
C
D
A,1
D,5
D,4
D,4
Outgoing link
to use, cost
destination
Distance table
Routing table
Notes: <number>
<footer>
<header>
<date/time>

## Slide 21: Distance Vector Algorithm: example
X
Z
1
2
7
Y
D (Y,Z)
X
c(X,Z) + min {D (Y,w)}
w
=
=
7+1 = 8
Z
D (Z,Y)
X
c(X,Y) + min {D (Z,w)}
w
=
=
2+1 = 3
Y
Notes: <number>
<footer>
<header>
<date/time>

## Slide 22: Distance Vector Algorithm: example
X
Z
1
2
7
Y
Notes: <number>
<footer>
<header>
<date/time>

## Slide 23: Distance Vector: link cost changes
Link cost changes:
node detects local link cost change
updates distance table (line 15)
if cost change in least cost path, notify neighbors (lines 23,24)
X
Z
1
4
50
Y
1
algorithm
terminates
“good
news
travels
fast”
Notes: <number>
<footer>
<header>
<date/time>

## Slide 24: Distance Vector: link cost changes
Link cost changes:
good news travels fast
bad news travels slow - “count to infinity” problem!
X
Z
1
4
50
Y
60
algorithm
continues
on!
Notes: <number>
<footer>
<header>
<date/time>

## Slide 25: Distance Vector: poisoned reverse
If Z routes through Y to get to X :
Z tells Y its (Z’s) distance to X is infinite (so Y won’t route to X via Z)
will this completely solve count to infinity problem?
X
Z
1
4
50
Y
60
algorithm
terminates
Notes: <number>
<footer>
<header>
<date/time>

## Slide 26: OSPF
OSPF =Open Shortest Path First
Developed to address shortcomings of RIP
  has rapid, loop-free convergence
  does not count to infinity
Link metrics between 0 and 65,535, no limit on path metric
Is a “link state protocol”
Has reputation for being complex
Scales well
Defined in RFCs 1247 (1991), 1583 (1994), 2178 (1997), 2328 (1998).

## Slide 27: Link State Database
A
D
E
C
B
100
100
20
20
80
80
20
20
10
10
10
10
10
10
ME
Each Router has a database representing the entire network
that is constructed from the local knowledge at each router
B
D
A
C
80
100
20

## Slide 28: Building OSPF Routing Table
Compute locally using Link State Database!
A
D
E
C
B
100
100
20
20
80
80
20
20
10
10
10
10
10
10
ME
50
30
20
30
Dijkstra
Dest.
Nxt Hop
Metric
B
D
50
C
D
D
D
D
E
30
20
30

## Slide 29: That’s Easy!
Not so fast!
RIP RFC 1058 : 33 pages
OSPF RFC 2328 : 244 pages
Much of this
complexity is
related to the
synchronization of
the distributed,
replicated link state
database.
Plus network
modeling ….
Distance Vector vs. Link State….

## Slide 30: BGP-4
BGP = Border Gateway Protocol
Is an exterior routing protocol (EGP)
Is a Policy-Based routing protocol
Is the de facto EGP of today’s global Internet
Has a reputation for being complex
Supports hierarchical routing
Is a distance vector protocol
Notes: Is complex like OSPF. But much more scary. If you screw up, the whole interet will know!
ISPs and NSP employ many network engineers provide care and
feeding of BGP.

## Slide 31: BGP Intro
BGP4 is the protocol used on the Internet to exchange routing information between providers, and to propagate external routing information through networks.
Each autonomous network is called an Autonomous System.
ASs which inject routing information on their own behalf have ASNs.

## Slide 32: BGP Peering
BGP-speaking routers peer with each other over TCP sessions, and exchange routes through the peering sessions.
Providers typically try to peer at multiple places. Either by peering with the same AS multiple times, or because some ASs are multi-homed, a typical network will have many candidate paths to a given prefix.

## Slide 33: The BGP Route
The BGP route is, conceptually, a “promise” to carry data to a section of IP space. The route is a “bag” of attributes.
The section of IP space is called the “prefix” attribute of the route.
As a BGP route travels from AS to AS, the ASN of each AS is stamped on it when it leaves that AS. Called the AS_PATH attribute, or “as-path” in Cisco-speak.

## Slide 34: BGP: a path vector protocol !
Customer E
ISP A (Tier 1)
ISP C
ISP D (Tier 2)
ISP B (Tier 1)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 35: BGP: a path vector protocol !
Customer E
ISP A (Tier 1)
ISP C
ISP B (Tier 1)
ISP D (Tier 2)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 36: BGP: a path vector protocol !
Notes: <number>
<footer>
<header>
<date/time>

## Slide 37: BGP: a path vector protocol !
Notes: <number>
<footer>
<header>
<date/time>

## Slide 38: BGP: doing it’s job…
Notes: <number>
<footer>
<header>
<date/time>

## Slide 39: BGP: doing it’s job…
Notes: <number>
<footer>
<header>
<date/time>

## Slide 40: BGP: doing it’s job…
Notes: <number>
<footer>
<header>
<date/time>

## Slide 41: BGP: doing it’s job…
Notes: <number>
<footer>
<header>
<date/time>

## Slide 42: Why policy should win over distance metrics???
ISP1
ISP2
ISP3
Cust1
Cust2
Cust3
Host 1
Host 2
YES!
NO!
Even if it is
the shortest
path!

## Slide 43: Current Internet Architecture
AS23
AS400
AS300
AS2006
AS1717
Arbitrary Internetwork
of Autonomous Systems
An Autonomous System
is a unified administrative
domain with a consistent
routing policy
Currently about 7000 AS
numbers are assigned,
about 4200 in use

## Slide 44: Policy : Transit vs. Nontransit
AS1
AS144
AS701
A nontransit AS allows
only traffic originating
from AS or traffic with
destination within AS
A transit AS allows traffic with neither
source nor destination within AS to flow
across the network
IP traffic
BBN
Bell Labs
UUnet

## Slide 45: Stub vs. Multihomed Networks
AS23
AS400
AS300
AS1717
Multihomed Networks
Stub Networks
AS2006
Multihomed
networks are
“required” to
run BGP

## Slide 46: AS topology
AS 1
AS 4
AS 5
XP
AS 3
AS 6
$$$
(peering)
A
B
$$$
AS 2
$$$
Notes: <number>
<footer>
<header>
<date/time>
Routes can have different values…
Assume peering AS 1 is peering with AS 4 + AS 5 -> EXPANCIVE upstream/transit is provided by AS 2.
you may want to prefer the cheaper peering links over the expensive transit links…
you may want to prefer european links over trans-atlantic links
a trans-atlantic cable over a satellite link, etc…
Communities give:
Easier control of where routes go.
Just a number (or numbers) that get stamped on BGP routes.
TELEKOM: Why important?
-> Communities make configuration and design easier.

## Slide 47: BGP design
Distance vector protocol
Implements policies to enable politics and traffic engineering
Decision process (in each router):

(modified) updates
out-policy filter
best path
selection
in-policy filter
updates 
in-policy filter
updates 
Notes: <number>
<footer>
<header>
<date/time>
BGP is a distance vector protocol:
operates on “rumors”,
Hey, I’ve heard that my neighbor can reach this or that destination.
Because the protocol is used even between the US and Afghanistan – there’s the need for policies (already discussed).
On the bottom of the page is a picture of how each router filters, tags or modifies updates.
TELEKOM: Why important?
->

## Slide 48: BGP attributes
Attributes are “knobs” for
  traffic engineering
  capacity planning
Communities:
  Used to group destinations to which routing decisions can be applied.
  Each destination can belong to multiple communities.
  Usually applied with route-maps.
Next Hop
AS Path
...
MED
Local-
Pref.
...
Community
Notes: <number>
<footer>
<header>
<date/time>
Next-Hop => where to send the traffic
AS path => loop detection (Arne)
Beside policies BGP has some knobs, for directing traffic: (TE)
Why Interdomain Traffic engineering?
-> Alleviating congestion on edge links
-> Adapting to provisioning changes (e.g., link capacity)
-> Achieving good end-to-end performance
Weight -> directing traffic this way (local in a router)
Local-Pref -> -”- within an AS.
MED -> Tells the neighbor on which ingress I like my traffic.
and communities.
-> Communities provide the possibility to tag routes,
several routes can be stamped and
decisions can be made more easily based on that stamp.
TELEKOM: Why important?
-> To know what knobs big-T can turn to improve T-network

## Slide 49: BGP Route Attributes
In addition to the prefix, the as-path, and the next-hop, the BGP route has other attributes, affectionately known as “knobs and twiddles” -
  local-pref, sometimes used - “hammer”
  origin code, rarely used
  MED (“metric”) - a gentle nudge

## Slide 50: AS Path Attribute
AS1
135.104.0.0/16
AS Path = 144
135.104.0.0/16
AS Path = 144
AS701
Alternet (Uunet)
AS702
Alternet (Uunet)
135.104.0.0/16
AS Path = 701 144
135.104.0.0/16
AS Path = 702 701 144
AS1849
Uunet UK
BBN
AS5413
GXN
135.104.0.0/16
AS Path = 1 144
AS5459
LINX
135.104.0.0/16
AS Path = 5413 1 144
135.104.0.0/16
AS Path = 5459 5413 1 144
AS144
135.104.0.0/16
Bell Labs
Route Originated
Notes: This was constructed by looking at actual BGP route tables obtained from the route view project at ISI.
Of course, only the AS Path attribute is shown here.
LINX = London Internet Exchange. A NAP for UK. See http://www.linx.net/
not for profit partnership between Internet Service Providers in UK,
50 members, including Uunet UK and GXN.
GXN = GX Networks, a London ISP. See http://www.gxn.net/
Uunet UK, see http://www.uk.uu.net/
Guess which route Uunet UK announced?

## Slide 51
Sequence of AS(s) a route has traversed.
Provides a mechanism for loop detection.
Policies may be applied
based on AS path.
Local AS added only when
send to external peer.
Shortest AS path preferred
AS Path
AS3847
207.240.0.0/16
AS1673
140.222.0.0/16
AS701 192.67.95.0/24
AS3561
204.70.0.0/15
192.67.95.0/24 3847 701 i
140.222.0.0 3847 1673 i
204.70.0.0/15 3847 3561 i
207.240.0.0/16 3847 i
AS6201
E
C
F
G
D
B
A

## Slide 52
Next-hop IP address to
reach a network.
Router A will advertise 198.3.97.0/24 to router B with a next-hop of 207.240.24.202.
With IBGP, the next-hop does not change.
IGPs should carry route to next-hops, using intelligent forwarding decision.
AS 6201
AS 3847
198.3.97.0/24
A
B
207.240.24.200/30
.201
A
B
.202
C
Next Hop

## Slide 53
Local Preference
Local to AS
Used to influence BGP
path selection
Default 100
Highest local-pref preferred
AS 6201
208.1.1.0/24
A
B
208.1.1.0/24 100
Preferred by all
AS3847 routers
208.1.1.0/24 80
AS 3847
G
F
E
C
D

## Slide 54: iBGP Peers Must be Fully Meshed
eBGP update
iBGP updates
iBGP peers do not announce
routes received via iBGP
N border routers means N(N-1)/2 peering sessions -- this does not scale
Currently three solutions :
  Break an AS up into smaller Autonomous Systems
  Route Reflectors
  Confederations

## Slide 55: Tim Griffin: “BGP Wedgies”
Customer E
ISP A (Tier 1)
ISP C
ISP D (Tier 2)
ISP B (Tier 1)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 56: Tim Griffin: “BGP Wedgies”
Customer E
ISP A (Tier 1)
ISP C
ISP D (Tier 2)
ISP B (Tier 1)
primary link
backup link
Notes: <number>
<footer>
<header>
<date/time>

## Slide 57: Desired Situation !!!
Customer E
ISP A (Tier 1)
ISP C
ISP D (Tier 2)
ISP B (Tier 1)
backup link
primary link
Notes: <number>
<footer>
<header>
<date/time>

## Slide 58: AS path prepending ???
AS 2
ISP A (Tier 1)
ISP C
ISP D (Tier 2)
ISP B (Tier 1)
“2“
“2 2 2 2 2“
Notes: <number>
<footer>
<header>
<date/time>

## Slide 59: Policies with “communities” ?!!
AS 2
ISP A (Tier 1)
ISP C
ISP D (Tier 2)
ISP B (Tier 1)
Community: set local-preference
primary link
Notes: <number>
<footer>
<header>
<date/time>

## Slide 60: Primary link fails…
AS 2
ISP A (Tier 1)
ISP C
ISP D (Tier 2)
ISP B (Tier 1)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 61: “Primary link” recovers ?!!
AS 2
ISP A (Tier 1)
ISP C
ISP D (Tier 2)
ISP B (Tier 1)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 62: BGP Operations Simplified
Establish Peering on
TCP port 179
Peers Exchange
All Routes
Exchange Incremental
Updates
AS1
AS2
While connection
is ALIVE exchange
route UPDATE messages
BGP
BGP Route =
network prefix + attributes
Notes: BGP speaking routers exchange information with their BGP peers.
Peers are configured by network engineer.

## Slide 63: BGP Route Processing
Best Route
Selection
Apply Import
Policies
BGP Route
Table
Apply Export
Policies
Install Best Routes
Receive
BGP
Updates
Best and
Alternate
Routes
Apply policies
only to
Best Routes!
Transmit
BGP
Updates
Apply Policy =
filter routes &
tweak attributes
Based on
Attribute
Values
Only this is
Detailed in
RFC 1771
IP Forwarding Table
Notes: BGP NEVER accepts a route as ASYYY that has YYY in its AS_PATH.
Since an AS only announces its best routes, this means that each router hears at most N best routes for any destination, where N is the number of peers.
Note : some vendors have implemented route filters for RIP and OSPF.

## Slide 64: BGP Best Route Selection Process
When two routes with the same network prefix ...
1) Pick route with highest
LOCAL PREFERENCE
2) Pick route with shortest
AS PATH
3) Pick route with lowest MED
4) Pick route with closest NEXT HOP (via IGP)
5) Pick route from router with
lowest IP address (break tie)
Allows policy
to override
distance metric
Notes: Note : not all atts are used (pure “filter” atts).
Vendor specific atts may get mixed in here.
Note how local pref overrides all other considerations.

## Slide 65: Recommended Reading
www.cambridge.intel-research.net/~tgriffin/interdomain/
Internet Routing Architectures. Bassam Halabi. 1997. [The BGP Bible!]
BGP4: Inter-domain Routing in the Internet. John W. Stewart, III. 1999. [Good high-level introduction.]
Routing in the Internet. Christian Huitema. 1995.
OSPF -- Anatomy of an Internet Routing Protocol. John T. Moy. 1998.
Interconnections : Bridges and Routers. Radia Perlman. 1992.
Managing IP Networks with Cisco Routers. Scott M. Ballew. 1997.